## Slide 1
Warm Ups: AnswerCell
Your cell phone rings. Return true if you should answer it. Normally you answer, except in the morning you only answer if it is your mom calling. In all cases, if you are asleep, you do not answer.
isMom (m): 1 if it is mom
0 if not mom
isMorning (a): 1 if it is morning
0 if not morning
isAsleep (s): 1 if asleep
0 if not asleep
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
m
a
s
AnswerCell
1
1
1
0
0
0
0
0
!m!a!s
m!a!s
ma!s
!m&&!a&&!s||m&&!a&&!s||m&&a&&!s
Or simplified a bit
!s&&((!m&&!a)||(m&&!a)||(m&&a))

## Slide 2: This method isn’t necessarily restricted to bools as long as you can simplify the inputs into two states. The children in Cleveland spend most of the day playing outside. In particular, they play if the temperature is between 60 and 90 (inclusive). Unless it is summer, then the upper limit is 100 instead of 90. Given an int temperature and a boolean isSummer, return true if the children play and false otherwise.

## Slide 3: More Resources
Lesson: https://www.allaboutcircuits.com/textbook/digital/chpt-7/converting-truth-tables-boolean-expressions/
Truth Table -> Logic Expression Converter:
http://www.32x8.com/
Logic Expression Simplifier: http://www.dcode.fr/boolean-expressions-calculator